## Slide 1
Design Conceptual Aircraft
via SUAVE
Student Lecturer: Lin Yi
Date：March 17, 2026
Email：linyi@mail.nwpu.edu.cn
Notes: Hello every one，I’m Lin Yi. Today we will talk about how to design conceptual aircraft using SUAVE.
Aircraft design and SUAVE are both really complex. I can’t make you a SUAVE expert or an aircraft design expert just with this one class. It’s just impossible. So like I said, today we are just having a discussion. If you have any questions, or if you think I’ve said something wrong during class, just interrupt me any time.

## Slide 2
content
Background Introduction
Prepare
Overall Design Process
  Design Flowchart
  Case Implementation
Main Modules
  Vehicle
  Mission
  Aerodynamic Analysis
Customization & Extension
Notes: Here is what we’ll do today. We’ll start with a background of SUAVE, then I will help you install the suave, run a test case, and build your first case yourself. After that, I will introduce some main modules of SUAVE so that you can have a deeper insight into this code. If we have extra time, I will show some examples of how to create custom modules.

## Slide 3
1、Background Introduction
SUAVE is a conceptual level aircraft design environment built with the ability to analyze and optimize both conventional and unconventional designs. This capability is achieved in part by allowing analysis information for aircraft to be drawn from multiple sources. Many other software tools for aircraft conceptual design rely on fixed empirical correlations and other handbook approximation. SUAVE instead provides a framework that can be used to design aircraft featuring advanced technologies by augmenting relevant correlations with physics-based methods.
Notes: So let’s start with SUAVE’s background first. SUAVE is a conceptual level aircraft design environment built with the ability to analyze and optimize both conventional and unconventional designs, Blah blah blah. You have probably noticed this is the official intro from its website, so I’m not gonna read it word by word, just focus on this line, “SUAVE provides a framework”. To me, I’d rather call it a code style, a style to make code highly encapsulated and modularized. You can assemble these modules however you want, modify’em, rewrite’em or even create your own with your idea. Alright, sorry I went off track a bit. Anyway it’s a super customizable program. Let’s dive in.

## Slide 4
2、Prepare
cmd
conda create –n suave python = 3.60
conda activate suave
Libraries | version
matplotlib | 3.3.4
numpy | 1.16.6
scipy | 1.2.3
scikit-learn | 0.18.2
plotly | 5.18.0
openvsp | 3.29.1
1、Prepare the Anaconda
2、Create python environment
3、Install libraries the suave need
cmd
pip install –r requirement.txt
or
cmd
pip install numpy==1.16.6
...
4、Download suave
suavecode/SUAVE: An Aircraft Design Toolbox
suavecode/Tutorials: This is where the tutorial scripts live
Notes: So the first thing we should do is to install the python environment for SUAVE. I believe you have downloaded the Anaconda before this class ok? That will make things more easy.

## Slide 5
2、Prepare
4、Download suave
suavecode/SUAVE: An Aircraft Design Toolbox
suavecode/Tutorials: This is where the tutorial scripts live
Git bash
git clone https://github.com/suavecode/SUAVE.git
or
Download the zip from release directly
5、Install suave
GitHub repository
cmd
cd D:\SUAVE-2.5.2\trunk ##change the path
python3 setup.py install
Notes: Once we set up a working environment for SUAVE, we can download the code from the github. Maybe you can not use the git clone, just download the zip file. Then run a command to install it.

## Slide 6
  Test if you setup SUAVE successfully
B737-800 in openvsp
Run the tut_mission_B737.py to see these pictures as shown above
2、Prepare
Notes: Open the Tutorial folder, find the tut_mission_B737.py script, run it and just wait a minute — I think it’ll take about one minute. Then you’ll see lots of plots fill your whole screen! Like this, altitude, weight, lift, drag… all kinds of information will pop up right in front of you. don’t worry. We’ll go through these plots together later. this is just to check if you’ve installed SUAVE correctly. If you don’t see those plots, just let me know. Alright? Alright, we’ve got SUAVE installed.

## Slide 7
3、Overall Design Process
What do we need to design for an aircraft?
Requirements
Mission
Configuration
Analysis
Aerodynamic
Weight
Thrust
Stability
…
Notes: Before we start working on our first SUAVE case, we first need to understand what conceptual aircraft design is, or more simply, what steps we need to go through. This is the overall conceptual design process; it’s not super formal, but it includes all the key steps. First, we need to figure out our aircraft requirements: whether we’re designing a fighter jet, helicopter or transport aircraft, how many missiles the fighter carries, if the helicopter is for rescue or combat missions, and what range the transport aircraft needs. These are all our basic requirements. Once we confirm the requirements, we define the whole flight mission, including takeoff, climb, cruise, descent, landing and other possible mission phases. After setting up the mission, we calculate initial aircraft parameters with standard formulas, such as maximum takeoff weight using the Breguet formula. Then we sketch out the aircraft layout. I mean sketch, not final design — at this point we don’t have any detailed aircraft data, the aircraft doesn’t even exist yet. We can model it in OpenVSP, or even just draw it on a napkin, and use our imagination to build our own aircraft. After that we do analyses like aerodynamics, weight updates and thrust analysis, and check if our aircraft can finish the mission. If not, we go back and adjust the design repeatedly until it meets the requirements. You’ve already learned all this aircraft design knowledge from Professor Zhang, so I won’t talk too much about it, and now let’s focus on how to use SUAVE in this whole design process.

## Slide 8
def main():
vehicle = vehicle_setup()
configs = configs_setup(vehicle)
configs_analyses = analyses_setup(configs)
analyses = SUAVE.Analyses.Analysis.Container()
analyses.configs = configs_analyses
simple_sizing(configs)
configs.finalize()
analyses.finalize()
mission = analyses.mission
results = mission.evaluate() plot_mission(results)
return
3、Overall Design Process - Build the main function
🛠️ Config Setup
Create analysis config
Main function: encapsulates aircraft, analysis, mission, and post-processing modules.
🧮 Mission Calculate
Run the mission and plot the result
✈️ Simple sizing
Complete basic settings of vehicle
Notes: So we will firstly build the main function. And we can create several component functions to handle specific operation of the aircraft, like aerodynamic module, or vehicle setup function, maybe we will write some aircraft parameters in this function later. So in this stage we just create and type the “pass” in these component functions, just to make sure this script can be runned normally later.

## Slide 9
3、Overall Design Process - Define the Analyses
def base_analysis(vehicle):
analyses = SUAVE.Analyses.Vehicle()
weights = SUAVE.Analyses.Weights.Weights_Transport()
weights.vehicle = vehicle
analyses.append(weights)
aerodynamics = SUAVE.Analyses.Aerodynamics.Fidelity_Zero()
aerodynamics.geometry = vehicle
analyses.append(aerodynamics)
energy = SUAVE.Analyses.Energy.Energy()
energy.network = vehicle.networks
analyses.append(energy)
planet = SUAVE.Analyses.Planets.Planet()
analyses.append(planet)
atmosphere = SUAVE.Analyses.Atmospheric.US_Standard_1976()
atmosphere.features.planet = planet.features
analyses.append(atmosphere)
return analyses
Base analysis: create analysis component and set aerodynamic solver.
🛠️ Basic setting
No need to modify usually
🔍Aerodynamic solver
This cases uses vortex
🔍Weights module
Calculate weight change by fuel
Notes: Once we have finished the main function, the basic framework for aircraft design, the first module will be developed is the base_analysis function. To start we need to define the output of this function, we want this function can return a analyses module so that we can use it to analysis the aerodynamic character of our aircraft in other steps. We create a a class in the first line of this function. Then we add all of the necessary components in turns. The weight module will update the total weight during the flight mission, the second part for base_analyses function is most important, we choose the aerodynamic method in this part, in this case we just choose the Fidelity_Zero() module, because this module calculate quickly, is suitable for our class, you can just get results in several seconds. Now we add the energy module, the planet module and the atmosphere module into this function so that it can run correctly.

## Slide 10
def analyses_setup(configs):
analyses = SUAVE.Analyses.Analysis.Container()
for tag,config in configs.items():
analysis = base_analysis(config)
analyses[tag] = analysis
return analyses
def configs_setup(vehicle):
configs = SUAVE.Components.Configs.Config.Container()
base_config = SUAVE.Components.Configs.Config(vehicle)
base_config.tag = 'base'
configs.append(base_config)
return configs
3、Overall Design Process - Define the Analyses
Analyses_setup and configs_setup:
Set tag for analysis component,
if you have more than one analysis component you can call them by different tags.
🛠️ Basic setting
Transfer vehicle to analysis component

## Slide 11
3、Overall Design Process - Define the mission
def mission_setup(analyses):
mission = SUAVE.Analyses.Mission.Sequential_Segments()
mission.tag = 'simple_mission'
airport = SUAVE.Attributes.Airports.Airport()
airport.altitude = 0.0 * Units.km
airport.delta_isa = 0.0
airport.atmosphere =
SUAVE.Attributes.Atmospheres.Earth.US_Standard_1976()
mission.airport = airport
Mission_setup:
Define the flight mission, including takeoff, climb, cruise, descent, land
🔍Airport setting
Sometime will need to modify, like takeoff from plateau

## Slide 12
Segments = SUAVE.Analyses.Mission.Segments
base_segment = Segments.Segment()
segment = Segments.Climb.Constant_Speed_Constant_Rate(base_segment)
segment.tag = "climb"
segment.analyses.extend( analyses.base )
segment.altitude_start = 0.0 * Units.km
segment.altitude_end = 10.668 * Units.km
segment.air_speed = 160.0 * Units['m/s']
segment.climb_rate = 6.0 * Units['m/s’]
mission.append_segment(segment)
3、Overall Design Process - Define the mission
🛠️Basic segments class
Define the takeoff

## Slide 13
segment = Segments.Cruise.Constant_Speed_Constant_Altitude(base_segment)
segment.tag = "cruise"
segment.analyses.extend( analyses.base )
segment.air_speed = 230.412 * Units['m/s']
segment.distance = 2490. * Units.nautical_miles
mission.append_segment(segment)
3、Overall Design Process - Define the mission
Define the cruise

## Slide 14
segment = Segments.Descent.Constant_Speed_Constant_Rate(base_segment)
segment.tag = "descent"
segment.analyses.extend( analyses.base )
segment.altitude_end = 0.0 * Units.km
segment.air_speed = 160.0 * Units['m/s']
segment.descent_rate = 6.0 * Units['m/s’]
mission.append_segment(segment)
return mission
3、Overall Design Process - Define the mission
Define the descent

## Slide 15
3、Overall Design Process - Create the Vehicle
def vehicle_setup():
vehicle = SUAVE.Vehicle()
vehicle.tag = 'Boeing_737-800'
vehicle.mass_properties.max_takeoff = 79015.8 * Units.kg
vehicle.mass_properties.takeoff = 79015.8 * Units.kg
vehicle.mass_properties.operating_empty = 62746.4 * Units.kg
vehicle.mass_properties.max_zero_fuel = 62732.0 * Units.kg
vehicle.mass_properties.cargo = 10000. * Units.kg
vehicle.envelope.ultimate_load = 3.75
vehicle.envelope.limit_load = 2.5
vehicle.reference_area = 124.862 * Units['meters**2']
vehicle.passengers = 170
vehicle.systems.control = "fully powered"
vehicle.systems.accessories = "medium range"
Overall parameter

## Slide 16
Main Wing
wing = SUAVE.Components.Wings.Main_Wing()
wing.tag = 'main_wing'
wing.aspect_ratio = 10.18
wing.sweeps.quarter_chord = 25 * Units.deg
wing.thickness_to_chord = 0.1
wing.taper = 0.1
wing.spans.projected = 34.32 * Units.meter
wing.chords.root = 7.760 * Units.meter
wing.chords.tip = 0.782 * Units.meter
wing.chords.mean_aerodynamic = 4.235 * Units.meter
wing.areas.reference = 124.862 * Units['meters**2']
wing.twists.root = 4.0 * Units.degrees
wing.twists.tip = 0.0 * Units.degrees
wing.origin = [[13.61, 0, -1.27]] * Units.meter
wing.vertical = False
wing.symmetric = True
vehicle.append_component(wing)
3、Overall Design Process - Create the Vehicle

## Slide 17
Horizontal Tail
wing = SUAVE.Components.Wings.Horizontal_Tail()
wing.tag = 'horizontal_stabilizer'
wing.aspect_ratio = 6.16
wing.sweeps.quarter_chord = 40.0 * Units.deg
wing.thickness_to_chord = 0.08
wing.taper = 0.2
wing.spans.projected = 14.2 * Units.meter
wing.chords.root = 4.7 * Units.meter
wing.chords.tip = 0.955 * Units.meter
wing.chords.mean_aerodynamic = 3.0 * Units.meter
wing.areas.reference = 32.488 * Units['meters**2']
wing.twists.root = 3.0 * Units.degrees
wing.twists.tip = 3.0 * Units.degrees
wing.origin = [[32.83 * Units.meter,
0 , 1.14 * Units.meter]]
wing.vertical = False
wing.symmetric = True
vehicle.append_component(wing)
3、Overall Design Process - Create the Vehicle

## Slide 18
Vertical Tail
wing = SUAVE.Components.Wings.Vertical_Tail()
wing.tag = 'vertical_stabilizer'
wing.aspect_ratio = 1.91
wing.sweeps.quarter_chord = 25. * Units.deg
wing.thickness_to_chord = 0.08
wing.taper = 0.25
wing.spans.projected = 7.777 * Units.meter
wing.chords.root = 8.19 * Units.meter
wing.chords.tip = 0.95 * Units.meter
wing.chords.mean_aerodynamic = 4.0 * Units.meter
wing.areas.reference = 27.316 * Units['meters**2']
wing.twists.root = 0.0 * Units.degrees
wing.twists.tip = 0.0 * Units.degrees
wing.origin = [[28.79, 0, 1.54]] * Units.meter
wing.vertical = True
wing.symmetric = False
vehicle.append_component(wing)
3、Overall Design Process - Create the Vehicle

## Slide 19
Fuselage
fuselage = SUAVE.Components.Fuselages.Fuselage()
fuselage.tag = 'fuselage'
fuselage.fineness.nose = 1.6
fuselage.fineness.tail = 2.
fuselage.lengths.nose = 6.4 * Units.meter
fuselage.lengths.tail = 8.0 * Units.meter
fuselage.lengths.total = 38.02 * Units.meter
fuselage.lengths.fore_space = 6. * Units.meter
fuselage.lengths.aft_space = 5. * Units.meter
fuselage.width = 3.74 * Units.meter
fuselage.heights.maximum = 3.74 * Units.meter
fuselage.effective_diameter = 3.74 * Units.meter
fuselage.areas.side_projected = 142.1948 * Units['meters**2']
fuselage.areas.wetted = 446.718 * Units['meters**2']
fuselage.areas.front_projected = 12.57 * Units['meters**2']
fuselage.differential_pressure = 5.0e4 * Units.pascal
vehicle.append_component(fuselage)
3、Overall Design Process - Create the Vehicle

## Slide 20
Nacelle
nacelle = SUAVE.Components.Nacelles.Nacelle()
nacelle.tag = 'nacelle_1'
nacelle.length = 2.71
nacelle.inlet_diameter = 1.90
nacelle.diameter = 2.05
nacelle.areas.wetted = 1.1*np.pi*nacelle.diameter*nacelle.length
nacelle.origin = [[13.72, -4.86,-1.9]]
nacelle.flow_through = True
nacelle_airfoil = SUAVE.Components.Airfoils.Airfoil()
nacelle_airfoil.naca_4_series_airfoil = '2410'
nacelle.append_airfoil(nacelle_airfoil)
nacelle_2 = deepcopy(nacelle)
nacelle_2.tag = 'nacelle_2'
nacelle_2.origin = [[13.72, 4.86,-1.9]]
vehicle.append_component(nacelle)
vehicle.append_component(nacelle_2)
3、Overall Design Process - Create the Vehicle

## Slide 21
Turbofan Network
3、Overall Design Process - Create the Vehicle
turbofan = SUAVE.Components.Energy.Networks.Turbofan()
turbofan.tag = 'turbofan'
turbofan.number_of_engines = 2
turbofan.bypass_ratio = 5.4
turbofan.origin =
[[13.72, 4.86,-1.9],[13.72, -4.86,-1.9]] * Units.meter
turbofan.working_fluid = SUAVE.Attributes.Gases.Air()
Air ➡️ Ram ➡️ Inlet Nozzle ➡️ Fan ➡️ Low Pressure Compressor ➡️
High Pressure Compressor ➡️ Combustor ➡️ High Pressure Turbine ➡️
Low Pressure Turbine ➡️ Core Nozzle / Fan Nozzle ➡️ Thrust

## Slide 22
Turbofan Network
3、Overall Design Process - Create the Vehicle
ram = SUAVE.Components.Energy.Converters.Ram()
ram.tag = 'ram'
turbofan.append(ram)
inlet_nozzle =
SUAVE.Components.Energy.Converters.Compression_Nozzle()
inlet_nozzle.tag = 'inlet_nozzle'
inlet_nozzle.polytropic_efficiency = 0.98
inlet_nozzle.pressure_ratio = 0.98
turbofan.append(inlet_nozzle)
Air ➡️ Ram ➡️ Inlet Nozzle ➡️ Fan ➡️ Low Pressure Compressor ➡️
High Pressure Compressor ➡️ Combustor ➡️ High Pressure Turbine ➡️
Low Pressure Turbine ➡️ Core Nozzle / Fan Nozzle ➡️ Thrust

## Slide 23
Turbofan Network
3、Overall Design Process - Create the Vehicle
fan = SUAVE.Components.Energy.Converters.Fan()
fan.tag = 'fan'
fan.polytropic_efficiency = 0.93
fan.pressure_ratio = 1.7
turbofan.append(fan)
compressor =
SUAVE.Components.Energy.Converters.Compressor()
compressor.tag = 'low_pressure_compressor'
compressor.polytropic_efficiency = 0.91
compressor.pressure_ratio = 1.14
turbofan.append(compressor)
Air ➡️ Ram ➡️ Inlet Nozzle ➡️ Fan ➡️ Low Pressure Compressor ➡️
High Pressure Compressor ➡️ Combustor ➡️ High Pressure Turbine ➡️
Low Pressure Turbine ➡️ Core Nozzle / Fan Nozzle ➡️ Thrust

## Slide 24
Turbofan Network
3、Overall Design Process - Create the Vehicle
compressor =
SUAVE.Components.Energy.Converters.Compressor()
compressor.tag = 'high_pressure_compressor'
compressor.polytropic_efficiency = 0.91
compressor.pressure_ratio = 13.415
turbofan.append(compressor)
Air ➡️ Ram ➡️ Inlet Nozzle ➡️ Fan ➡️ Low Pressure Compressor ➡️
High Pressure Compressor ➡️ Combustor ➡️ High Pressure Turbine ➡️
Low Pressure Turbine ➡️ Core Nozzle / Fan Nozzle ➡️ Thrust

## Slide 25
Turbofan Network
3、Overall Design Process - Create the Vehicle
combustor =
SUAVE.Components.Energy.Converters.Combustor()
combustor.tag = 'combustor'
combustor.efficiency = 0.99
combustor.alphac = 1.0
combustor.turbine_inlet_temperature = 1450 # K
combustor.pressure_ratio = 0.95
combustor.fuel_data =
SUAVE.Attributes.Propellants.Jet_A()
turbofan.append(combustor)
Air ➡️ Ram ➡️ Inlet Nozzle ➡️ Fan ➡️ Low Pressure Compressor ➡️
High Pressure Compressor ➡️ Combustor ➡️ High Pressure Turbine ➡️
Low Pressure Turbine ➡️ Core Nozzle / Fan Nozzle ➡️ Thrust

## Slide 26
Turbofan Network
3、Overall Design Process - Create the Vehicle
turbine = SUAVE.Components.Energy.Converters.Turbine()
turbine.tag='high_pressure_turbine'
turbine.mechanical_efficiency = 0.99
turbine.polytropic_efficiency = 0.93
turbofan.append(turbine)
turbine = SUAVE.Components.Energy.Converters.Turbine()
turbine.tag='low_pressure_turbine'
turbine.mechanical_efficiency = 0.99
turbine.polytropic_efficiency = 0.93
turbofan.append(turbine)
Air ➡️ Ram ➡️ Inlet Nozzle ➡️ Fan ➡️ Low Pressure Compressor ➡️
High Pressure Compressor ➡️ Combustor ➡️ High Pressure Turbine ➡️
Low Pressure Turbine ➡️ Core Nozzle / Fan Nozzle ➡️ Thrust

## Slide 27
Turbofan Network
3、Overall Design Process - Create the Vehicle
nozzle =
SUAVE.Components.Energy.Converters.Expansion_Nozzle()
nozzle.tag = 'core_nozzle'
nozzle.polytropic_efficiency = 0.95
nozzle.pressure_ratio = 0.99
turbofan.append(nozzle)
===========================================================
nozzle =
SUAVE.Components.Energy.Converters.Expansion_Nozzle()
nozzle.tag = 'fan_nozzle'
nozzle.polytropic_efficiency = 0.95
nozzle.pressure_ratio = 0.99
turbofan.append(nozzle)
Air ➡️ Ram ➡️ Inlet Nozzle ➡️ Fan ➡️ Low Pressure Compressor ➡️
High Pressure Compressor ➡️ Combustor ➡️ High Pressure Turbine ➡️
Low Pressure Turbine ➡️ Core Nozzle / Fan Nozzle ➡️ Thrust

## Slide 28
Turbofan Network
3、Overall Design Process - Create the Vehicle
thrust = SUAVE.Components.Energy.Processes.Thrust()
thrust.tag ='compute_thrust'
thrust.total_design = 2*24000. * Units.N
turbofan.thrust = thrust
altitude = 35000.0*Units.ft
mach_number = 0.78
Determine turbofan behavior at the design condition
turbofan_sizing(turbofan,mach_number,altitude)
vehicle.append_component(turbofan)
return vehicle
Air ➡️ Ram ➡️ Inlet Nozzle ➡️ Fan ➡️ Low Pressure Compressor ➡️
High Pressure Compressor ➡️ Combustor ➡️ High Pressure Turbine ➡️
Low Pressure Turbine ➡️ Core Nozzle / Fan Nozzle ➡️ Thrust

## Slide 29
Simple sizing
3、Overall Design Process - Create the Vehicle
def simple_sizing(configs):
base = configs.base
base.pull_base()
base.mass_properties.max_zero_fuel =
0.9 * base.mass_properties.max_takeoff
for wing in base.wings:
wing.areas.wetted = 2.0 * wing.areas.reference
wing.areas.exposed = 0.8 * wing.areas.wetted
wing.areas.affected = 0.6 * wing.areas.wetted
base.store_diff()
return
Simple sizing: This function automatically computes unspecified critical parameters for the vehicle using overall design inputs, finalizing the aircraft model for subsequent analysis.

## Slide 30
3、Overall Design Process - Plot the result
def plot_mission(results,line_style='bo-'):
plot_flight_conditions(results, line_style)
plot_aerodynamic_forces(results, line_style)
plot_aerodynamic_coefficients(results, line_style)
plot_drag_components(results, line_style)
plot_altitude_sfc_weight(results, line_style)
plot_aircraft_velocities(results, line_style)
return
plot_mission:
Plot mission result by matplotlib

## Slide 31
4、Main Modules - Vehicle
1、Download openvsp==3.29.1
cmd
cd D:\OpenVSP-3.29.1-win64\python ##change the path
pip install -r requirements.txt
add
from SUAVE.Input_Output.OpenVSP import write
to the import section
add
write(vehicle, 'base')
after vehicle_setup() in main()
Run your code again, “base.vsp3”will be generated under your code directory

## Slide 32
4、Main Modules - Vehicle
# Create the wing
wing_id = vsp.AddGeom( "WING" )
vsp.SetGeomName(wing_id, wing.tag)
area_tags[wing.tag] = ['wings',wing.tag]
x_secs = []
x_sec_curves = []
for i_segs in range(0,n_segments+2):
x_secs.append('XSec_' + str(i_segs))
x_sec_curves.append('XSecCurve_' + str(i_segs))
vsp.SetParmVal( wing_id,'X_Rel_Location','XForm',wing_x)
vsp.SetParmVal( wing_id,'Y_Rel_Location','XForm',wing_y)
vsp.SetParmVal( wing_id,'Z_Rel_Location','XForm',wing_z)
Partial source code of vsp_write
How SUAVE create the aircraft geometry

## Slide 33
4、Main Modules - Vehicle
How OpenVSP create the aircraft geometry
Partial text of vsp file
wing.sweeps.quarter_chord=25
wing.thickness_to_chord =0.1
wing.taper =0.1
wing.spans.projected =34.32
wing.chords.root =7.760
wing.chords.tip =0.782
OpenVSP uses XML format to record geometric parameters of each component with structured tags.

## Slide 34
Flight Mission
4、Main Modules - Mission
Takeoff & Climb
Cruise
Descent & landing
If you want your flight mission to be more realistic, you should adopt a multi-segment climb and descent mode to achieve smoother speed transitions and configure distinct aircraft states for takeoff and landing.

## Slide 35
4、Main Modules – Aerodynamic Analysis
Fidelity_Zero | Based on VLM method, it is suitable for aerodynamic force calculation of low-speed aircraft.
Supersonic_Zero | Also based on VLM method, but modified with empirical formulas for supersonic conditions.
AERODAS | An airfoil aerodynamic prediction method developed by NASA. Its core function is to calculate the CL and CD of airfoils over the entire angle of attack range through empirical formulas and curve fitting.
SU2_Euler | Generate volume meshes via Gmsh, run CFD simulations in SU2.
Supersonic_OpenVSP_Wave_Drag | Call the wave_drag method in openvsp
Lifting_Line | Lift line theory

## Slide 36
5、Customization & Extension
How to optimize your aircraft via SUAVE

## Slide 37
Thank You！
Student Lecturer: Lin Yi
Date：March 17, 2026
Email：linyi@mail.nwpu.edu.cn